國立中山大學應用數學系

(Dept. of Applied Math., National Sun Yat-sen University)

Talk

Speaker：楊德良 教授

台灣大學土木工程學系

Title：Analysis of Multi-dimensional Burgers’ Equations by the Method of Fundamental Solutions

Time：2005/12/22（星期四, Thu）15：30 ~ 16：30

Place：理學院4樓理4009-1室(教室設備：白板、固定單槍、固定電腦)

(Room 4009-1, Dept. of Applied Math, NSYSU)

Tea Time：15：00~15:30於理4010室 (系辦公室)

Abstract

The Eulerian-Lagrangian method of fundamental solutions is proposed to solve the multi-dimensional unsteady Burgers’ equations in this study. Depending upon the Eulerian-Lagrangian method, the quasi-linear Burgers’ equations can be converted to the linear diffusion equations. The diffusion fundamental solution is adopted by the method of fundamental solutions to solve the diffusion equations; meanwhile, the convective term is dealt with by the back-tracking scheme along the characteristics. The proposed numerical scheme, which is free from mesh generation and numerical integral, is a truly meshless method. Multi-dimensional Burgers’ equations are analyzed by the proposed meshless method and the numerical results are compared well with the analytical solutions. By observing these results, the proposed numerical scheme is believed to be an accurate and simple method for the solutions of the unsteady multi-dimensional Burgers’ equations which are characterized by the physics of shock propagation and turbulence modeling.

國立中山大學應用數學系 敬啟

演講查詢網址：http://www.math.nsysu.edu.tw/seminar/semi.html

交通查詢網址： http://www.math.nsysu.edu.tw/department/map.html

敬 請 公 告！ 歡 迎 參 加！